## Slide 1: Small Scale Fading

## Slide 2: Small Scale Fading/ Fading
The rapid fluctuations of received signal strength over short time intervals or travel distances.
Caused by interference from multiple copies of Tx signal arriving at Rx at slightly different times.
Three most important effects:
  Rapid changes in signal strengths over small travel distances or short time periods.
  Random frequency modulation due to varying Doppler shifts on different multipath signals
  Time dispersion (echoes) caused by multipath propagation delays.
Notes: Small scale fading or simply fading. Signal strength = amplitude
2. Changes in the frequency of signals.
3. Multiple signals arriving a different times. When added together at the antenna, signals are spread out in time. This can cause a interference between bits that are received.

## Slide 3: Factors Influencing Small-Scale Fading
1) Multipath Propagation
  The presence of reflecting objects and scatterers in the space between transmitter and receiver creates a constantly changing channel environment
  Causes the signal at receiver to fade or distort
2) Speed of Mobile
  Relative motion between base station and mobile causes random frequency modulation due to Doppler shift (fd)
  Different multipath components may have different frequency shifts.
Notes: Relative motion is the calculation of the motion of an object with regard to some other moving object.

## Slide 4: Factors Influencing Small-Scale Fading
3) Speed of Surrounding Objects
  If the speed of surrounding objects is greater than mobile, the fading is dominated by those objects
  If the surrounding objects are slower than the mobile, then their effect can be ignored
4) The transmission bandwidth of the signal
  Depending on the relation between the signal bandwidth and the coherence bandwidth of the channel, the signal is either distorted or faded
  If the signal bandwidth is greater than coherence bandwidth it creates distortion
  If the signal bandwidth is smaller than coherence bandwidth it create small scale fading
Notes: the bandwidth of the channel can be quantified by the coherence bandwidth which is related to the specific multipath structure of the channel. The coherence bandwidth is a measure of the maximum frequency difference for which signals are still strongly correlated in amplitude.

## Slide 5: Doppler Effect/Shift
When a transmitter or receiver is moving, the frequency of the received signal changes. It is different than the frequency of transmission. This is called Doppler Effect.
The change in frequency is called Doppler shift
The Doppler shift is positive
  If the mobile is moving towards the direction of arrival of the signal.
The Doppler shift is negative
  If the mobile is moving away from the direction of arrival of the signal.
Notes: See 20121212.. Pdf

## Slide 6: Doppler Shift – Receiver is moving
Notes: Apparent = actual

## Slide 7: Example – 4.3:
Consider a transmitter which radiates a sinusoidal carrier frequency of 1850 MHz. For a vehicle moving 60 mph, compute the received carrier frequency if the mobile is moving
(a) directly towards the transmitter,
(b) directly away from the transmitter,
(c) in a direction which is perpendicular to the direction of arrival of the transmitted signal.
Notes: 1 mile = 1609.344m
60 mile = 96560.64m/hr = 26.8224m/sec
1 hr = 60x60 sec

## Slide 8: Impulse response of Multipath channel
The small scale variations of a mobile radio signal can be directly related to the impulse response of mobile radio channel.
Impulse response contains all information necessary to
  Simulate the channel
  Analyze the channel
A mobile radio channel may be modeled as a linear filter with a time varying impulse response
Notes: It is the response(output) from a system (or process) when you put an 'impulse (unit pulse, delta function)' as an input. It is because it fully characterize a system. If you know the impulse response of a system, you can figure out the response (output) of the system for any kind of input without even testing it.
Casual system : https://books.google.com.bd/books?id=ZZeYb-GASbMC&pg=SA2-PA51&dq=Impulse+Response+Model+of+a+Multipath+Channel&hl=en&sa=X&ved=0ahUKEwiV36qsn77hAhUp8HMBHUHgDoUQ6AEIOTAD#v=onepage&q=Impulse%20Response%20Model%20of%20a%20Multipath%20Channel&f=false

## Slide 9: Impulse Response Model:

## Slide 10
Since the receiver moves along the ground at a constant velocity v, the position of the receiver can by expressed as
Since v is a constant, y(vt, t) is just a function of t. Therefore,
From equation, it is clear that the mobile radio channel can be modeled as a linear time varying channel, where the channel changes with time and distance.

## Slide 13: Power Delay Profile

## Slide 14: Time Dispersion Parameters
The time dispersion parameters that can be determined from a power delay profile are
  mean excess delay
  rms delay spread
  excess delay spread
To quantify “how spread-out” the arriving signals are, we use time dispersion parameters
Notes: Dispersion = spreading

## Slide 15: Time Dispersion Parameters
Notes: Dispersion = spreading
the second moment of the mean excess delay

## Slide 16: Time Dispersion Parameters: Max Excess Delay(X dB)
Notes: Dispersion = spreading
the second moment of the mean excess delay

## Slide 17
Notes: Dispersion = spreading
the second moment of the mean excess delay

## Slide 18
Notes: Dispersion = spreading
the second moment of the mean excess delay

## Slide 19: Coherence Bandwidth (Bc)
Bc : statistical measure of frequency range where MRC response is flat
    MRC response is flat = passes all frequencies with ≈ equal gain & linear phase
    Amplitudes of different frequency components are correlated
    If two sinusoids have frequency separation greater than Bc, they are affected quite differently by the channel
    Estimates coherence BW (Bc )
      0.9 correlation → Bc ≈ 1 / 50 (signals are above 90% correlated with each other)
      0.5 correlation → Bc ≈ 1 / 5 (signals are above 50% correlated with each other)
Notes: Dispersion = spreading
the second moment of the mean excess delay

## Slide 20: Coherence Time (Tc)
Coherence time is the time duration over which the channel impulse response is essentially invariant.
If the symbol period of the baseband signal is greater the coherence time, than the signal will distort.
Coherence time is also defined as:
where fm is the maximum Doppler spread given by
TS
TC
Notes: See 20121212.. Pdf

## Slide 21: Example
Notes: V = 88 ft/s
Tc = 9/16pifm = 9/16x3.14x77 = 2.3 ms
Fm = v/lemda = 88/1.142 = 77 Hz
Lemda = c / f =9.8 x 10^8/ 860 x 10^6 = 1.1442 ft
Ts = 10^6/19200 = 5.2 micro s

## Slide 22: Doppler Spread (BD)
Measure of spectral broadening caused by motion
We know how to compute Doppler shift: fd
Doppler spread, BD, is defined as the maximum Doppler shift: fm = v/λ
If the baseband signal bandwidth is much greater than BD then effect of Doppler spread is negligible at the receiver.
Notes: See 20121212.. Pdf

## Slide 23: Types of small-scale fading

## Slide 24: Flat Fading
Occurs when symbol period of the transmitted signal is much larger than the Delay Spread of the channel
  Bandwidth of the applied signal is narrow.
  If Bs  Bc , and Ts    Flat fading
May cause deep fades.
  require 20 or 30 dB more power to achieve low BER during times of deep fades.
  Increase the transmit power to combat this situation.
Flat fading channels are known as amplitude varying channels or narrow-band channels.
A rule of thumb that channel is assumed to be flat fading if Ts > 10
All frequencies undergone the same amount of fading
Notes: 24

## Slide 25: Frequency Selective Fading
Occurs when channel multipath delay spread is greater than the symbol period.
  If Bs >> Bc , and Ts <<   Frequency selective fading
  Channel induces Intersymbol Interference (ISI)
Frequency selective fading channels are known as wideband channels since the BW of the signal is wider than the BW of the channel impulse response.
A rule of thumb that channel is assumed to be frequency selective fading if Ts <= 10
Not all frequencies undergone the same amount of fading.
Notes: 25

## Slide 26: Example
From the previous calculation of PDP, would the channel be regarded as a wideband channel for a binary data system with data rate of 25 Kbits/sec?
If the data rate is 25  103 bits/sec, then the symbol period TS is:
It is found previously that RMS = 1.08 sec, so rule of thumb 10RMS  10 sec
Hence, the channel can regards as narrowband flat fading since TS >> 10RMS
What is the maximum data rate for the system to be ISI-free? (For ISI-free, TS >10RMS condition must be fulfilled)
Since 10RMS is about 10 sec, then the minimum symbol period TS must not be less than 10 sec. Therefore, we can write that TS = 10 sec
Hence, the maximum data rate is: 1/TS = 1/(1010-6) = 100Kbits/sec, for ISI-free system

## Slide 27: Example
Can the channel considered as narrowband when the data rate in the previous example is increased to 200Kbits/sec?
If the data rate is 200  103 bits/sec, then the symbol period TS is:
We know from previously that 10RMS  10 sec which is greater than TS
Therefore, the channel can no longer considered as narrowband since TS < 10RMS . Hence, a wideband frequency selective fading channel.

## Slide 28: Fast Fading
Due to Doppler Spread
  Rate of change of the channel characteristics is larger than the Rate of change of the transmitted signal
  The channel changes during a symbol period.
  The channel changes because of receiver motion.
  Coherence time of the channel is smaller than
  the symbol period of the transmitter signal
  It causes frequency dispersion due to Doppler spread and leads to distortion.
Occurs when:
BS < BD
and
TS > TC
Notes: 28

## Slide 29: Slow Fading
Due to Doppler Spread
  Rate of change of the channel characteristics is much smaller than the rate of change of the transmitted signal
Occurs when:
BS >> BD
and
TS << TC
BS: Bandwidth of the signal BD: Doppler Spread
TS: Symbol Period TC: Coherence Bandwidth
Notes: 29

## Slide 30: Summary of Channel Classification
1) Frequency Flat (no delay-spread) & Time-Flat (slow fading) Channel
BS << BC TS << TC
or or
TS >> rms BS >> BD
(Doubly –flat fading channel)
2) Frequency Flat (no delay-spread) & Time-Selective (fast fading) Channel
BS << BC TS > TC
or or
TS >> rms BS < BD
(Fast-varying flat fading channel)
3) Frequency Selective (Delay-spread) & Time-Flat (slow fading) Channel
BS > BC TS << TC
or or
TS < rms BS >> BD
(Slow-varying frequency selective channel)
4) Frequency Selective (Delay-spread) & Time-Selective (fast fading) Channel
BS > BC TS > TC
or or
TS < rms BS < BD
(Doubly dispersive fading channel)
BS = Bandwidth of the baseband signal TS = Symbol duration of the baseband signal
BC = Coherence bandwidth of the channel TC = Coherence time of the channel
BD = Doppler spread of the channel rms = RMS delay spread of the channel

## Slide 31: Example
Notes: See 20121212.. Pdf

## Slide 32: Example