## Slide 1
Work Measurement

## Slide 2
Work study is the systematic examination of the methods of carrying on activities so as to improve the effective use of resources and to set up standards of performance for the activities being carried out
Method study the systematic recording and critical examination of existing and proposed ways of doing work as a means of developing and applying easier and more effective methods and reducing costs.
Work Measurement is measuring time it should take a qualified worker to complete a specified task, working at a sustainable rate, using given methods, tools and equipment, raw material inputs, and workplace arrangement

## Slide 3: Meaningful Standards Help a firm to Determine-
Staffing needs( to meet required production)
Cost and time estimates prior to production
Crew size and work balance(who does what in an assembly line)
Expected production(to constitute a fair day’s work)
Basis of wage-incentive plans(provides a reasonable incentive)
Efficiency of employees and supervision(standard is necessary to determine)
Work Measurement || Slide 3 of 28
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 4: Labor Standards
Four ways of establishing labor standards:
Historical experience
Time studies
Predetermined time standards
Work sampling
Work Measurement || Slide 2 of 28

## Slide 5: Historical Experience
How the task was performed last time
Easy and inexpensive
Data available from production records or time cards
Data is not objective and may be inaccurate
Not recommended
Work Measurement || Slide 4 of 28

## Slide 6: Time Studies
Involves timing a sample of a worker’s
performance and using it to set a standard
Requires trained and experienced observers
Cannot be set before the work is performed
Work Measurement || Slide 5 of 28

## Slide 7: Time Studies
Define the task to be studied
Divide the task into precise elements
Decide how many times to measure the task
Time and record element times and rating of performance
Work Measurement || Slide 6 of 28

## Slide 8: Time Studies
Compute average observed time
Average observed
time
Sum of the times recorded to perform each element
Number of observations
=
Determine performance rating and normal time
Normal time = x
Average
observed time
Performance
rating factor
Work Measurement || Slide 7 of 28

## Slide 9: Time Studies
Add the normal times for each element to develop the total normal time for the task
Compute the standard time
Standard time =
Total normal time
1 - Allowance factor
Work Measurement || Slide 8 of 28

## Slide 10: Rest Allowances
Personal time allowance
  4% - 7% of total time for use of restroom, water fountain, etc.
Delay allowance
  Based upon actual delays that occur
Fatigue allowance
  Based on human energy expenditure under various physical and environmental conditions
Work Measurement || Slide 9 of 28

## Slide 11: Time Study Example 1
Average observed time = 4.0 minutes
Worker rating = 85%
Allowance factor = 13%
Standard time??

## Slide 12: Time Study Example 1
Average observed time = 4.0 minutes
Worker rating = 85%
Allowance factor = 13%
Normal time = (Average observed time) x (Rating factor)
= (4.0)(.85)
= 3.4 minutes
Standard time = = =
Normal time
1 - Allowance factor
3.4
1 - .13
3.4
.87
= 3.9 minutes
Work Measurement || Slide 10 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 13: Time Study Example 2
Allowance factor = 15%
 | OBSERVATIONS (MIN) |  |  |  |  | PERFORMANCE RATING
JOB ELEMENT | 1 | 2 | 3 | 4 | 5 | 
(A) Compose and type letter | 8 | 10 | 9 | 21* | 11 | 120%
(B) Type envelope address | 2 | 3 | 2 | 1 | 3 | 105%
(C) Stuff, stamp, and seal envelopes | 2 | 1 | 5* | 2 | 1 | 110%
Calculate Standard Time

## Slide 14: Time Study Example 2
Allowance factor = 15%
Delete unusual or nonrecurring observations (marked with *)
Compute average times for each element
Average time for A = (8 + 10 + 9 + 11)/4 = 9.5 minutes
Average time for B = (2 + 3 + 2 + 1 + 3)/5 = 2.2 minutes
Average time for C = (2 + 1 + 2 + 1)/4 = 1.5 minutes
 | OBSERVATIONS (MIN) |  |  |  |  | PERFORMANCE RATING
JOB ELEMENT | 1 | 2 | 3 | 4 | 5 | 
(A) Compose and type letter | 8 | 10 | 9 | 21* | 11 | 120%
(B) Type envelope address | 2 | 3 | 2 | 1 | 3 | 105%
(C) Stuff, stamp, and seal envelopes | 2 | 1 | 5* | 2 | 1 | 110%
Work Measurement || Slide 11 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 15: Time Study Example 2
Compute the normal time for each element
Normal time for A = (9.5)(1.2) = 11.4 minutes
Normal time for B = (2.2)(1.05) = 2.31 minutes
Normal time for C = (1.5)(1.10) = 1.65 minutes
Normal time = (Average observed time) x (Rating)
Add the normal times to find the total normal time
Total normal time = 11.40 + 2.31 + 1.65
= 15.36 minutes
Work Measurement || Slide 12 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 16
5. Standard time for the job:
Standard time = Total normal time/( 1 - Allowance factor)
= 15.36/(1-.15)
=18.07 min
Thus, 18.07 minutes is the time standard for this job.

## Slide 17: Predetermined Time Standards
Divide manual work into small basic elements that have established times
Can be done in a laboratory away from the actual production operation
Can be set before the work is actually performed
No performance ratings are necessary
Work Measurement || Slide 19 of 28
Notes: You might point out to students that this slide links capacity to work measurement (standard times).

## Slide 18
Thank You