## Slide 1
© 2008 Prentice Hall, Inc.
15 – 1
“Scheduling”
Sadia Hasanat
Lecturer
Department of Mechanical and Production Engineering
Ahsanullah University of Science and Technology
IPE 4111: Industrial Management

## Slide 2: Learning Outcome
© 2008 Prentice Hall, Inc.
15 – 2
At the end of this lecture the students should be able to explain scheduling, priority rules of scheduling
At the end of this lecture the students should be able to describe types of scheduling
At the end of this lecture the students should be able to calculate different priority rules of scheduling
At the end of this lecture the students should be able to solve Johnson’s Rule

## Slide 3: Scheduling
© 2008 Prentice Hall, Inc.
15 – 4
Scheduling means Establishing the
timing of the use of equipment,
facilities, and human activities in
an organization

## Slide 4
Type of Scheduling
A work location in which a number of general purpose work stations exist and are used to perform a variety of jobs
Flow-shop scheduling is a special case of job-shop scheduling where there is strict order of all operations to be performed on all jobs
Flow-shop scheduling
Job-shop scheduling
Notes: Demand, customization, complexity of workflow, amount of setup

## Slide 5: Sequencing Jobs
© 2008 Prentice Hall, Inc.
15 – 21
Specifies the order in which jobs should be performed at work centers
Priority rules are used to dispatch or sequence jobs
  FCFS: First come, first served
  SPT: Shortest processing time
  EDD: Earliest due date
  LPT: Longest processing time

## Slide 6: Priority Rules for Dispatching Jobs
© 2008 Prentice Hall, Inc.
15 – 22
First come, first served
The first job to arrive at a work center is processed first
Earliest due date
The job with the earliest due date is processed first
Shortest processing time
The job with the shortest processing time is processed first
Longest processing time
The job with the longest processing time is processed first

## Slide 7: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 23
Job | Job Work (Processing) Time (Days) | Job Due Date (Days)
A | 6 | 8
B | 2 | 6
C | 8 | 18
D | 3 | 15
E | 9 | 23
Apply the four popular sequencing rules to these five jobs

## Slide 8: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 24
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
A | 6 | 6 | 8 | 0
B | 2 | 8 | 6 | 2
C | 8 | 16 | 18 | 0
D | 3 | 19 | 15 | 4
E | 9 | 28 | 23 | 5
 | 28 | 77 |  | 11
FCFS: Sequence A-B-C-D-E

## Slide 9
Sequencing Example
FCFS: Sequence A-B-C-D-E
Average completion time = Sum of total flow time =
Number of jobs
Total job work time
Utilization = Sum of total flow time =
= Sum of total flow time =
Total job work time
Average job lateness =
Total late days
Number of jobs
=
Average number of jobs in the system

## Slide 10: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 25
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
A 6 6 8 0
B 2 8 6 2
C 8 16 18 0
D 3 19 15 4
E 9 28 23 5
28 77 11
FCFS: Sequence A-B-C-D-E
Average completion time = Sum of total flow time = 77/5 = 15.4 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/77 = 36.4%
Average number of = Sum of total flow time = 77/28 = 2.75 jobs
Total job work time
Average job lateness =
= 11/5 = 2.2 days
Total late days
Number of jobs

## Slide 11: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 26
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
D | 3 | 5 | 15 | 0
A | 6 | 11 | 8 | 3
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 65 |  | 9
SPT: Sequence B-D-A-C-E

## Slide 12: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 27
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
B 2 2 6 0
D 3 5 15 0
A 6 11 8 3
C 8 19 18 1
E 9 28 23 5
28 65 9
SPT: Sequence B-D-A-C-E
Average completion time = Sum of total flow time = 65/5 = 13 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/65 = 43.1%
Average number of = Sum of total flow time = 65/28 = 2.32 jobs
Total job work time
Average job lateness =
= 9/5 = 1.8 days
Total late days
Number of jobs

## Slide 13: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 28
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
A | 6 | 8 | 8 | 0
D | 3 | 11 | 15 | 0
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 68 |  | 6
EDD: Sequence B-A-D-C-E

## Slide 14: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 29
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
B 2 2 6 0
A 6 8 8 0
D 3 11 15 0
C 8 19 18 1
E 9 28 23 5
28 68 6
EDD: Sequence B-A-D-C-E
Average completion time = Sum of total flow time = 68/5 = 13.6 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/68 = 41.2%
Average number of = Sum of total flow time = 68/28 = 2.43 jobs
Total job work time
Average job lateness =
= 6/5 = 1.2 days
Total late days
Number of jobs

## Slide 15: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 30
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
E | 9 | 9 | 23 | 0
C | 8 | 17 | 18 | 0
A | 6 | 23 | 8 | 15
D | 3 | 26 | 15 | 11
B | 2 | 28 | 6 | 22
 | 28 | 103 |  | 48
LPT: Sequence E-C-A-D-B

## Slide 16: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 31
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
E 9 9 23 0
C 8 17 18 0
A 6 23 8 15
D 3 26 15 11
B 2 28 6 22
28 103 48
LPT: Sequence E-C-A-D-B
Average completion time = Sum of total flow time = 103/5 = 20.6 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/103 = 27.2%
Average number of = Sum of total flow time = 103/28 = 3.68 jobs
Total job work time
Average job lateness =
= 48/5 = 9.6 days
Total late days
Number of jobs

## Slide 17: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 32
Rule | Average Completion Time (Days) | Utilization (%) | Average Number of Jobs in System | Average Lateness (Days)
FCFS | 15.4 | 36.4 | 2.75 | 2.2
SPT | 13.0 | 43.1 | 2.32 | 1.8
EDD | 13.6 | 41.2 | 2.43 | 1.2
LPT | 20.6 | 27.2 | 3.68 | 9.6
Summary of Rules

## Slide 18: Comparison of Sequencing Rules
© 2008 Prentice Hall, Inc.
15 – 33
 No one sequencing rule excels on all criteria

SPT does well on minimizing flow time and
number of jobs in the system
But SPT moves long jobs to the end which may result in dissatisfied customers
FCFS does not do especially well (or poorly) on any criteria but is perceived as fair by customers
EDD minimizes lateness

## Slide 19: Sequencing N Jobs on Two Machines: Johnson’s Rule
© 2008 Prentice Hall, Inc.
15 – 38
Works with two or more jobs that pass through the same two machines or work centers
Minimizes total production time and idle time

## Slide 20: Johnson’s Rule
© 2008 Prentice Hall, Inc.
15 – 39
List all jobs and times for each work center
Choose the job with the shortest activity time. If that time is in the first work center, schedule the job first. If it is in the second work center, schedule the job last.
Once a job is scheduled, it is eliminated from the list
Repeat steps 2 and 3 working toward the center of the sequence

## Slide 21: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 40
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 22: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 41
B
E
D
C
A
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 23: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 42
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28
33
WC 1 | B | E | D | C | A | 
WC 2 |  |  |  |  |  | 
B
A
C
D
E

## Slide 24: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 43
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28
33
Time 0
B
A
C
D
E
B
A
C
D
E
WC
1
WC
2
1 3 5 7 9 10 11 12 13 17 19 21 22 2325 27 29 31 33 35
B
E
D
C
A
B
A
C
D
E

## Slide 25
THANK YOU !