## Slide 1
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 2
2
Ahsanullah University of Science & Technology
What is Inventory??
Inventory is stock or store of goods
3 types of Inventory
Raw material
Work-in-process
Finished goods
MROs (Maintenance, Repair, and Operating Materials)
IPE 4111: Industrial Management

## Slide 3
Dependent demand
Ahsanullah University of Science & Technology
Independent demand
3
Independent demand - the demand for item is independent of the demand for any other item in inventory
Dependent demand - the demand for item is dependent upon the demand for some other item in the inventory
IPE 4111: Industrial Management

## Slide 4
To meet anticipated demand
To smooth production requirements – seasonal
To protect against stock outs
To take advantages of quantity discounts
4
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 5
5
Ahsanullah University of Science & Technology
Inadequate control of inventories can result in both under and overstocking of items
The overall objective of inventory management is to achieve satisfactory levels of customer service while keeping inventory costs within reasonable bounds.
The timing
Size of orders
IPE 4111: Industrial Management

## Slide 6
Holding (carrying) cost
Cost to carry an item in inventory for a length of time.
Ordering costs
Costs of ordering and receiving inventory.
Setup costs
The costs involved in preparing equipment for a job.
Shortage costs
Costs resulting when demand exceeds the supply of inventory; often unrealized profit per unit.
**Lead time: Time interval between ordering and receiving the order.
8
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 7
ABC Analysis
Classifies inventory items according to some measure of importance and then allocates control efforts accordingly.
The origin of ABC analysis is “The Pareto Principle” which is named after an Italian economist Vilfredo Pareto, also called as 80/20 rule. This principle suggests that 80% of the total output is generated only by 20% of the valuable efforts.
9
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 8
Typically, three classes of items:
  A (very important)
  B (moderately important)
  C (least important)
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 9
11
Ahsanullah University of Science & Technology
s 60-70% value
ributes 20-30% value
0-70% contributes 5-10% value
Quantity
Cost
A | Class A: 10-15% contribute |  | 
 | B | Class B: 20-30% cont | 
 |  | C | Class C: 6
IPE 4111: Industrial Management

## Slide 10
12
Ahsanullah University of Science & Technology
A manager has obtained a list of unit costs and estimated annual demands for 10 inventory items and now wants to categorize the items on an A-B-C basis.
IPE 4111: Industrial Management
Items
Annual Demand
Cost per unit(£)
Boxes of Paperclip
Boxes of staples
Correcting fluid
Diaries
Erasers
Notepads
Pencils
Pens
Rulers
Staplers
21,000
10,000
16,000
50,000
15,000
40,000
80,000
1,20,000
15,000
10,000
0.50
0.50
1.50
3.50
0.10
2.0
0.03
0.05
0.25
1.50

## Slide 11
13
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 12
14
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 13
15
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 14
16
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 15
17
Ahsanullah University of Science & Technology
Cost
Class A
Class B
Class C
23% 13%
64% Quantity
80
IPE 4111: Industrial Management

## Slide 16
18
Ahsanullah University of Science & Technology
Need to determine when and how much to order
The basic economic order quantity model
The economic production quantity model
The quantity discount model
IPE 4111: Industrial Management

## Slide 17
ROP
LT
Time
Quantity
Ahsanullah University of Science & Technology
Usage rate
Maximum
inventory
level
Minimum inventory level
Place
order Receive
order
19
IPE 4111: Industrial Management

## Slide 18
EOQ is the order quantity that minimizes total cost
Assumptions
Only one product is involved
Annual demand requirements are known
Demand is spread evenly
Lead time does not vary
No quantity discount
20
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 19
Ahsanullah University of Science & Technology
𝑄
2
Annual Holding Cost, HC = 𝐻
𝑄
𝐷
Annual Ordering Cost, OC = 𝑆
𝑄 𝐷
2 𝑄
Total Cost, TC = 𝐻 + 𝑆
𝑄
𝐷
2 𝑄
Total Cost (including Material), TC = 𝐻 + 𝑆 +
𝐷 × 𝑃
𝑓𝑜𝑟 𝑀𝑖𝑛𝑖𝑚𝑢𝑚 𝐶𝑜𝑠𝑡, 𝑄 =
2𝐷𝑆
𝐻
Number of orders placed annually ×
Order cost per order
Average inventory level × Holding cost per unit per year
Material Cost
21
IPE 4111: Industrial Management

## Slide 20
Order Quantity
Annual
Cost
Ahsanullah University of Science & Technology
24
Holding Cost
Ordering Cost
Total Cost
Material Cost
EOQ

## Slide 21
Ahsanullah University of Science & Technology
25
(LT = 0)
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
a. Determine the optimal number of tires to order.
IPE 4111: Industrial Management

## Slide 22
Ahsanullah University of Science & Technology
𝑊𝑒 𝑘𝑛𝑜𝑤, 𝑄 =
2𝐷𝑆
𝐻
=
2 × 9600 ×75
16
= 300 tires per order
25
(LT = 0)
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
a. Determine the optimal number of tires to order.
IPE 4111: Industrial Management

## Slide 23
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
b. How many times per year does the store reorder?
26
IPE 4111: Industrial Management

## Slide 24
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
b. How many times per year does the store reorder?
We know,
Number of orders per year, N = =
𝐷 9600 𝑡𝑖𝑟𝑒𝑠/𝑦𝑟
𝑄 300 𝑡𝑖𝑟𝑒𝑠/𝑜𝑟𝑑𝑒𝑟
= 32 orders per year
26
IPE 4111: Industrial Management

## Slide 25
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
c. Determine the length of an order cycle or expected time between orders.
27
IPE 4111: Industrial Management

## Slide 26
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
c. Determine the length of an order cycle or expected time between orders.
Length of an order cycle =
𝑁𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝑤𝑜𝑟𝑘𝑖𝑛𝑔 𝑑𝑎𝑦𝑠 𝑝𝑒𝑟 𝑦𝑒𝑎𝑟
𝑁𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝑜𝑟𝑑𝑒𝑟𝑠 𝑝𝑒𝑟 𝑦𝑒𝑎𝑟, 𝑁
= 9 days
=
288
32
27
IPE 4111: Industrial Management

## Slide 27
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
d. Determine the annual Total cost.
8
IPE 4111: Industrial Management

## Slide 28
Ahsanullah University of Science & Technology
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and tread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
d. Determine the annual Total cost.
We know,
=2400 + 2400 = $4800
2
𝑄 𝐷
Total Cost, TC = 𝐻 +
Q
=
300
× 16 +
2 300
9600
× 75
8
IPE 4111: Industrial Management
𝑆

## Slide 29
Ahsanullah University of Science & Technology
29
(LT = 0)
Piddling Manufacturing assembles security monitors. It purchases 3,600 black-and-white cathode ray tubes a year at $65 each. Ordering costs are $31, and annual carrying costs are 20 percent of the purchase price.
a. Compute the optimal quantity and the total annual cost of ordering and carrying the inventory.
IPE 4111: Industrial Management

## Slide 30
Ahsanullah University of Science & Technology
𝑊𝑒 𝑘𝑛𝑜𝑤, 𝑄 =
= =
≈ 131 cathode ray tubes
2𝐷𝑆 2 × 3600 × 31 2 × 3600 × 31
𝐻
65 × 0.2 13
29
(LT = 0)
Piddling Manufacturing assembles security monitors. It purchases 3,600 black-and-white cathode ray tubes a year at $65 each. Ordering costs are $31, and annual carrying costs are 20 percent of the purchase price.
a. Compute the optimal quantity and the total annual cost of ordering and carrying the inventory.
IPE 4111: Industrial Management

## Slide 31
Ahsanullah University of Science & Technology
Piddling Manufacturing assembles security monitors. It purchases 3,600 black-and-white cathode ray tubes a year at $65 each. Ordering costs are $31, and annual carrying costs are 20 percent of the purchase price.
a. Compute the optimal quantity and the total annual cost of ordering and carrying the inventory.
30
IPE 4111: Industrial Management

## Slide 32
Ahsanullah University of Science & Technology
= $1704
2 𝑄
𝑄 𝐷
Total Cost, TC = 𝐻 + 𝑆
Piddling Manufacturing assembles security monitors. It purchases 3,600 black-and-white cathode ray tubes a year at $65 each. Ordering costs are $31, and annual carrying costs are 20 percent of the purchase price.
a. Compute the optimal quantity and the total annual cost of ordering and carrying the inventory.
We know,
=
2
131
× 13 +
131
3600
× 31
≈ 852 + 852
30
IPE 4111: Industrial Management

## Slide 33
A large bakery buys flour in 25-pound bags. The bakery uses an average of 1,215 bags a year. Preparing an order and receiving a shipment of flour involves a cost of $10 per order. Annual carrying costs are $75 per bag.
Determine the economic order quantity.
How many orders per year will there be?
Compute the total cost of ordering and carrying flour.
If holding costs were to increase by $9 per year, how much would that
affect the minimum total annual cost?
31
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management

## Slide 34
a. Economic Order Quantity:
32
Ahsanullah University of Science & Technology
𝑊𝑒 𝑘𝑛𝑜𝑤, 𝑄 =
=
2𝐷𝑆 2 × 1215 × 10
𝐻 75
= 18 bags per order
IPE 4111: Industrial Management

## Slide 35
b. Number of orders per year:
33
Ahsanullah University of Science & Technology
𝐷 1215
= = 𝟔𝟕. 𝟓
𝑄 18
c. Total cost:
= 675 + 675 = $1350
𝑄
𝐷
2 𝑄
TC = 𝐻 + 𝑆
18
= × 75
1215
2 18
+ × 10
IPE 4111: Industrial Management

## Slide 36
d. By increasing holding costs by $9 per year:
34
Ahsanullah University of Science & Technology
= 714 + 715 = $1429
Thus, total annual cost increases by $79
𝑄 𝐷
⸫ Total Cost, TC = 𝐻 + 𝑆
17
1215
2 𝑄 2 17
= × 84 + × 10
𝑄 =
=
2𝐷𝑆 2 × 1215 × 10
𝐻 75 + 9
= 17 bags per order
=
24300
84
IPE 4111: Industrial Management

## Slide 37
Ahsanullah University of Science & Technology
If demand and lead time are both constant, the reorder point is easy to calculate.
𝑅𝑂𝑃 = 𝑑 × 𝐿𝑇
Where,
d = Demand rate (units per day or week) LT = Lead time in days or weeks
IPE 4111: Industrial Management

## Slide 38
Ahsanullah University of Science & Technology
52
(LT ≠ 0)
Kevin takes Two-a-Day vitamins, which are delivered to his home by a routeman three days after an order is called in. At what point should Kevin reorder?
Usage rate = 2 vitamins per day
Lead time = 3 days
ROP = Usage rate × Lead time
= 2 vitamins per day × 3 days
= 6 vitamins
IPE 4111: Industrial Management

## Slide 39
Ahsanullah University of Science & Technology
Stock that is held in excess of expected demand due to variable demand and/or lead time.
𝑅𝑂𝑃 = 𝑑 × 𝐿𝑇 + 𝑠𝑠
Where,
d = Demand rate (units per day or week)
LT = Lead time in days or weeks ss = Safety Stock
IPE 4111: Industrial Management

## Slide 40
67
Ahsanullah University of Science & Technology
IPE 4111: Industrial Management
ABC Analysis Example

## Slide 41
67
Ahsanullah University of Science & Technology
Reference: Operations Management (11th edition) By William Stevenson (Chapter 13)
IPE 4111: Industrial Management