## Slide 1
© 2008 Prentice Hall, Inc.
15 – 1
“Scheduling”
Sadia Hasanat
Lecturer
Department of Mechanical and Production Engineering
Ahsanullah University of Science and Technology
IPE 4111: Industrial Management

## Slide 2: Learning Outcome
© 2008 Prentice Hall, Inc.
15 – 2
At the end of this lecture the students should be able to explain scheduling, priority rules of scheduling
At the end of this lecture the students should be able to describe types of scheduling
At the end of this lecture the students should be able to calculate different priority rules of scheduling
At the end of this lecture the students should be able to solve Johnson’s Rule

## Slide 3: Scheduling
© 2008 Prentice Hall, Inc.
15 – 4
Scheduling means Establishing the
timing of the use of equipment,
facilities, and human activities in
an organization

## Slide 4
Type of Scheduling
A work location in which a number of general purpose work stations exist and are used to perform a variety of jobs
Flow-shop scheduling is a special case of job-shop scheduling where there is strict order of all operations to be performed on all jobs
Flow-shop scheduling
Job-shop scheduling
Notes: Demand, customization, complexity of workflow, amount of setup

## Slide 5: Sequencing Jobs
© 2008 Prentice Hall, Inc.
15 – 21
Specifies the order in which jobs should be performed at work centers
Priority rules are used to dispatch or sequence jobs
  FCFS: First come, first served
  SPT: Shortest processing time
  EDD: Earliest due date
  LPT: Longest processing time

## Slide 6: Priority Rules for Dispatching Jobs
© 2008 Prentice Hall, Inc.
15 – 22
First come, first served
The first job to arrive at a work center is processed first
Earliest due date
The job with the earliest due date is processed first
Shortest processing time
The job with the shortest processing time is processed first
Longest processing time
The job with the longest processing time is processed first

## Slide 7: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 23
Job | Job Work (Processing) Time (Days) | Job Due Date (Days)
A | 6 | 8
B | 2 | 6
C | 8 | 18
D | 3 | 15
E | 9 | 23
Apply the four popular sequencing rules to these five jobs

## Slide 8: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 24
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
A | 6 | 6 | 8 | 0
B | 2 | 8 | 6 | 2
C | 8 | 16 | 18 | 0
D | 3 | 19 | 15 | 4
E | 9 | 28 | 23 | 5
 | 28 | 77 |  | 11
FCFS: Sequence A-B-C-D-E

## Slide 9
Sequencing Example
FCFS: Sequence A-B-C-D-E
Average completion time = Sum of total flow time =
Number of jobs
Total job work time
Utilization = Sum of total flow time =
= Sum of total flow time =
Total job work time
Average job lateness =
Total late days
Number of jobs
=
Average number of jobs in the system

## Slide 10: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 25
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
A 6 6 8 0
B 2 8 6 2
C 8 16 18 0
D 3 19 15 4
E 9 28 23 5
28 77 11
FCFS: Sequence A-B-C-D-E
Average completion time = Sum of total flow time = 77/5 = 15.4 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/77 = 36.4%
Average number of = Sum of total flow time = 77/28 = 2.75 jobs
Total job work time
Average job lateness =
= 11/5 = 2.2 days
Total late days
Number of jobs

## Slide 11: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 26
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
D | 3 | 5 | 15 | 0
A | 6 | 11 | 8 | 3
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 65 |  | 9
SPT: Sequence B-D-A-C-E

## Slide 12: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 27
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
B 2 2 6 0
D 3 5 15 0
A 6 11 8 3
C 8 19 18 1
E 9 28 23 5
28 65 9
SPT: Sequence B-D-A-C-E
Average completion time = Sum of total flow time = 65/5 = 13 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/65 = 43.1%
Average number of = Sum of total flow time = 65/28 = 2.32 jobs
Total job work time
Average job lateness =
= 9/5 = 1.8 days
Total late days
Number of jobs

## Slide 13: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 28
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
A | 6 | 8 | 8 | 0
D | 3 | 11 | 15 | 0
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 68 |  | 6
EDD: Sequence B-A-D-C-E

## Slide 14: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 29
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
B 2 2 6 0
A 6 8 8 0
D 3 11 15 0
C 8 19 18 1
E 9 28 23 5
28 68 6
EDD: Sequence B-A-D-C-E
Average completion time = Sum of total flow time = 68/5 = 13.6 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/68 = 41.2%
Average number of = Sum of total flow time = 68/28 = 2.43 jobs
Total job work time
Average job lateness =
= 6/5 = 1.2 days
Total late days
Number of jobs

## Slide 15: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 30
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
E | 9 | 9 | 23 | 0
C | 8 | 17 | 18 | 0
A | 6 | 23 | 8 | 15
D | 3 | 26 | 15 | 11
B | 2 | 28 | 6 | 22
 | 28 | 103 |  | 48
LPT: Sequence E-C-A-D-B

## Slide 16: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 31
Job Work
Job (Processing) Flow Job Due Job
Sequence Time Time Date Lateness
E 9 9 23 0
C 8 17 18 0
A 6 23 8 15
D 3 26 15 11
B 2 28 6 22
28 103 48
LPT: Sequence E-C-A-D-B
Average completion time = Sum of total flow time = 103/5 = 20.6 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/103 = 27.2%
Average number of = Sum of total flow time = 103/28 = 3.68 jobs
Total job work time
Average job lateness =
= 48/5 = 9.6 days
Total late days
Number of jobs

## Slide 17: Sequencing Example
© 2008 Prentice Hall, Inc.
15 – 32
Rule | Average Completion Time (Days) | Utilization (%) | Average Number of Jobs in System | Average Lateness (Days)
FCFS | 15.4 | 36.4 | 2.75 | 2.2
SPT | 13.0 | 43.1 | 2.32 | 1.8
EDD | 13.6 | 41.2 | 2.43 | 1.2
LPT | 20.6 | 27.2 | 3.68 | 9.6
Summary of Rules

## Slide 18: Comparison of Sequencing Rules
© 2008 Prentice Hall, Inc.
15 – 33
 No one sequencing rule excels on all criteria

SPT does well on minimizing flow time and
number of jobs in the system
But SPT moves long jobs to the end which may result in dissatisfied customers
FCFS does not do especially well (or poorly) on any criteria but is perceived as fair by customers
EDD minimizes lateness

## Slide 19: Sequencing N Jobs on Two Machines: Johnson’s Rule
© 2008 Prentice Hall, Inc.
15 – 38
Works with two or more jobs that pass through the same two machines or work centers
Minimizes total production time and idle time

## Slide 20: Johnson’s Rule
© 2008 Prentice Hall, Inc.
15 – 39
List all jobs and times for each work center
Choose the job with the shortest activity time. If that time is in the first work center, schedule the job first. If it is in the second work center, schedule the job last.
Once a job is scheduled, it is eliminated from the list
Repeat steps 2 and 3 working toward the center of the sequence

## Slide 21: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 40
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 22: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 41
B
E
D
C
A
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 23: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 42
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28
33
WC 1 | B | E | D | C | A | 
WC 2 |  |  |  |  |  | 
B
A
C
D
E

## Slide 24: Johnson’s Rule Example
© 2008 Prentice Hall, Inc.
15 – 43
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28
33
Time 0
B
A
C
D
E
B
A
C
D
E
WC
1
WC
2
1 3 5 7 9 10 11 12 13 17 19 21 22 2325 27 29 31 33 35
B
E
D
C
A
B
A
C
D
E

## Slide 25
THANK YOU !

## Slide 26
Work Measurement

## Slide 27
Work study is the systematic examination of the methods of carrying on activities so as to improve the effective use of resources and to set up standards of performance for the activities being carried out
Method study the systematic recording and critical examination of existing and proposed ways of doing work as a means of developing and applying easier and more effective methods and reducing costs.
Work Measurement is measuring time it should take a qualified worker to complete a specified task, working at a sustainable rate, using given methods, tools and equipment, raw material inputs, and workplace arrangement

## Slide 28: Meaningful Standards Help a firm to Determine-
Staffing needs( to meet required production)
Cost and time estimates prior to production
Crew size and work balance(who does what in an assembly line)
Expected production(to constitute a fair day’s work)
Basis of wage-incentive plans(provides a reasonable incentive)
Efficiency of employees and supervision(standard is necessary to determine)
Work Measurement || Slide 3 of 28
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 29: Labor Standards
Four ways of establishing labor standards:
Historical experience
Time studies
Predetermined time standards
Work sampling
Work Measurement || Slide 2 of 28

## Slide 30: Historical Experience
How the task was performed last time
Easy and inexpensive
Data available from production records or time cards
Data is not objective and may be inaccurate
Not recommended
Work Measurement || Slide 4 of 28

## Slide 31: Time Studies
Involves timing a sample of a worker’s
performance and using it to set a standard
Requires trained and experienced observers
Cannot be set before the work is performed
Work Measurement || Slide 5 of 28

## Slide 32: Time Studies
Define the task to be studied
Divide the task into precise elements
Decide how many times to measure the task
Time and record element times and rating of performance
Work Measurement || Slide 6 of 28

## Slide 33: Time Studies
Compute average observed time
Average observed
time
Sum of the times recorded to perform each element
Number of observations
=
Determine performance rating and normal time
Normal time = x
Average
observed time
Performance
rating factor
Work Measurement || Slide 7 of 28

## Slide 34: Time Studies
Add the normal times for each element to develop the total normal time for the task
Compute the standard time
Standard time =
Total normal time
1 - Allowance factor
Work Measurement || Slide 8 of 28

## Slide 35: Rest Allowances
Personal time allowance
  4% - 7% of total time for use of restroom, water fountain, etc.
Delay allowance
  Based upon actual delays that occur
Fatigue allowance
  Based on human energy expenditure under various physical and environmental conditions
Work Measurement || Slide 9 of 28

## Slide 36: Time Study Example 1
Average observed time = 4.0 minutes
Worker rating = 85%
Allowance factor = 13%
Standard time??

## Slide 37: Time Study Example 1
Average observed time = 4.0 minutes
Worker rating = 85%
Allowance factor = 13%
Normal time = (Average observed time) x (Rating factor)
= (4.0)(.85)
= 3.4 minutes
Standard time = = =
Normal time
1 - Allowance factor
3.4
1 - .13
3.4
.87
= 3.9 minutes
Work Measurement || Slide 10 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 38: Time Study Example 2
Allowance factor = 15%
 | OBSERVATIONS (MIN) |  |  |  |  | PERFORMANCE RATING
JOB ELEMENT | 1 | 2 | 3 | 4 | 5 | 
(A) Compose and type letter | 8 | 10 | 9 | 21* | 11 | 120%
(B) Type envelope address | 2 | 3 | 2 | 1 | 3 | 105%
(C) Stuff, stamp, and seal envelopes | 2 | 1 | 5* | 2 | 1 | 110%
Calculate Standard Time

## Slide 39: Time Study Example 2
Allowance factor = 15%
Delete unusual or nonrecurring observations (marked with *)
Compute average times for each element
Average time for A = (8 + 10 + 9 + 11)/4 = 9.5 minutes
Average time for B = (2 + 3 + 2 + 1 + 3)/5 = 2.2 minutes
Average time for C = (2 + 1 + 2 + 1)/4 = 1.5 minutes
 | OBSERVATIONS (MIN) |  |  |  |  | PERFORMANCE RATING
JOB ELEMENT | 1 | 2 | 3 | 4 | 5 | 
(A) Compose and type letter | 8 | 10 | 9 | 21* | 11 | 120%
(B) Type envelope address | 2 | 3 | 2 | 1 | 3 | 105%
(C) Stuff, stamp, and seal envelopes | 2 | 1 | 5* | 2 | 1 | 110%
Work Measurement || Slide 11 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 40: Time Study Example 2
Compute the normal time for each element
Normal time for A = (9.5)(1.2) = 11.4 minutes
Normal time for B = (2.2)(1.05) = 2.31 minutes
Normal time for C = (1.5)(1.10) = 1.65 minutes
Normal time = (Average observed time) x (Rating)
Add the normal times to find the total normal time
Total normal time = 11.40 + 2.31 + 1.65
= 15.36 minutes
Work Measurement || Slide 12 of 28
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 41
5. Standard time for the job:
Standard time = Total normal time/( 1 - Allowance factor)
= 15.36/(1-.15)
=18.07 min
Thus, 18.07 minutes is the time standard for this job.

## Slide 42: Predetermined Time Standards
Divide manual work into small basic elements that have established times
Can be done in a laboratory away from the actual production operation
Can be set before the work is actually performed
No performance ratings are necessary
Work Measurement || Slide 19 of 28
Notes: You might point out to students that this slide links capacity to work measurement (standard times).

## Slide 43
Thank You